## Slide 1: Course Code: CSE 303 Course Title: Data Communication
Green Networking Research Group
Dept. of Computer Science and Engineering, University of Dhaka

## Slide 2: Recommended book
Text Book:
Data Communications and Networking
Behrouz A. Forouzan,
4th EditionMcGraw-Hill
Reference Books:
Data and Computer Communications (8th Edition), William Stallings.
Computer Networks (5th Edition), Andrew S. Tanenbaum.

## Slide 3: Syllabus
Chapter 1 Introduction
Chapter 2 Network Models
Chapter 3 Data and Signals
Chapter 4 Digital Transmission
Chapter 5 Analog Transmission
Chapter 6 Bandwidth Utilization
Chapter 7 Transmission Media
Chapter 8 Switching
Chapter 9 High Speed Transmission Lines
Chapter 10 Error Detection and Correction

## Slide 4: Chapter 1. Introduction
Data communications
Networks
The Internet
Protocols and standards

## Slide 5: Data Communications
Data
  Information presented in whatever form is agreed upon by the parties creating and using the data
Data communication
  Exchange of data between two devices
  Via some form of transmission medium
Fundamental characteristics of data communication
  Delivery
  Accuracy
  Timeliness
  Jitter : Variation in the packet arrival time

## Slide 6: Five Components of Data Communication
Message: Information(data) to be communicated
Sender
Receiver
Transmission medium: Physical path by which a message travels
Protocol: A set of rules that govern data communication

## Slide 7: Direction of Data Flow

## Slide 8: Data Flow
Simplex
  Unidirectional
  As on a one-way street
Half-duplex
  Both transmit and receive possible, but not at the same time
  Like a one-lane road with two-directional traffic
  Walkie-talkie, CB radio
Full-duplex
  Transmit and receive simultaneously
  Like a two-way street, telephone network
  Channel capacity must be divided between two directions

## Slide 9: Network
Network: A set of devices (nodes) connected by communication links
Node: Computer, printer, or any device capable of sending and/or receiving data
To be considered effective and efficient, a network must meet a number of criteria

## Slide 10: Type of Connection

## Slide 11: Type of Connection
Point-to-point
  Dedicated link between two devices
  The entire capacity of the channel is reserved
  Ex) Microwave link, TV remote control
Multipoint
  More than two devices share a single link
  Capacity of the channel is either
    Spatially shared: Devices can use the link simultaneously
    Timeshare: Users take turns

## Slide 12: Physical Topology
Network Topology refers to layout of a network. How different nodes in a network are connected to each other and how they communicate is determined by the network's topology

## Slide 13: Mesh Topology
Dedicated point-to-point link to every other nodes
A mesh network with n nodes has n(n-1)/2 links. A node has n-1 I/O ports (links)
Advantages: No traffic problems, robust, security, easy fault identification & isolation
Disadvantages: Difficult installation/reconfiguration, space, cost

## Slide 14: Star Topology
Dedicated point-to-point link only to a central controller, called a hub
Hub acts as an exchange: No direct traffic between devices
Advantages: Less expensive, robust
Disadvantages: dependency of the whole on one single point, the hub
For a better idea watch this video : https://www.youtube.com/watch?v=1z0ULvg_pW8

## Slide 15: Bus Topology
One long cable that links all nodes
tap, drop line, cable end
limit on the # of devices, distance between nodes
Advantages: Easy installation, cheap
Disadvantages: Difficult reconfiguration, no fault isolation, a fault or break in the bus stops all transmission

## Slide 16: Ring Topology
Dedicated point-to-point link only with the two nodes on each sides
One direction, repeater
Advantages: Easy reconfiguration, fault isolation
Disadvantage: Unidirectional traffic, a break in the ring cab disable the entire network

## Slide 17: Hybrid Topology
Example: Main star topology with each branch connecting several stations in a bus topology
To share the advantages from various topologies

## Slide 18: Categories of Networks

## Slide 19: LAN
Usually privately owned
A network for a single office, building, or campus ≤ a few Km
Common LAN topologies: bus, ring, star
An isolated LAN connecting 12 computers to a hub in a closet

## Slide 20: MAN
Designed to extend to an entire city
Cable TV network, a company’s connected LANs
Owned by a private or a public company

## Slide 21: WAN
Long distance transmission, e.g., a country, a continent, the world
Enterprise network: A WAN that is owned and used by one company

## Slide 22: Internetwork
Internetwork (internet) : two or more networks are connected by internetworking devices
Internetworking devices: router, gateway, etc.
The Internet: a specific worldwide network

## Slide 23: Internetwork Example
A heterogeneous network : four WANs and two LANs

## Slide 24: The Internet
The Internet has revolutionized many aspects of our daily lives. It has affected the way we do business as well as the way we spend our leisure time. The Internet is a communication system that has brought a wealth of information to our fingertips and organized it for our use.
1967: ARPANET proposed by DoD’s ARPA(Advanced Research Project Agency)
1969: ARPANET in a reality: UCLA, UCSB, SRI, U. of Utah
1973: Vint Cerf and Bob Kahn propose TCP,
To split TCP into two protocols TCP and IP

## Slide 25: Internet Today
ISP (Internet service providers)
NISP (national ISP)
NAP (network access point)
Peering point

## Slide 26: Protocols
Protocol : rule
  A set of rules that govern data communication
  For communication to occur, entities must agree upon a protocol
  A protocol defines what is communicated, how is communicated and when is communicated.
Key elements of a protocol
  Syntax: structure or format of data
  Semantics: meaning of each section in the structure
  Timing: when and how fast data should be sent

## Slide 27: Standards: agreed-upon rules
Standards is essential in
  Creating/maintaining open and competitive markets
  Guaranteeing national/international interoperability
Two categories
  De jure (“by law” or “by regulation’) standards
  De facto (“by fact” or ‘by convention’) standards
  Proprietary standards: closed standards. Owned and controlled by one company.
  Nonproprietary standards: open standards. not registered or protected as a trademark or brand name
  proprietary standards are privately owned by one or more entities that control their distribution and access. Open standards let people and organizations set up new services and make them available across the rest of the Internet without permission.

## Slide 28: Standards Organizations
Standards are developed by
  Standards creation committees
  Forums
  Regulatory agencies
Standards committees & forums
  Standards committees are slow moving
  Forums are made up of interested corporations
  Forum are able to speed acceptance of a particular technology

## Slide 29: Standards Committees
ISO
  Voluntary international organization
ITU-T
  Formerly, CCITT formed by UN
ANSI
  Private non-profit corporation in the US
IEEE
  The largest engineering society in the world
EIA
  Non-profit organization in the US

## Slide 30: Internet Standards
An internet standard (STD) is a specification that has been approved by the Internet Engineering Task Force (IETF). Such standard helps to promote a consistent and universal use of the internet worldwide.
IETF (Internet Engineering Task Force)
Internet Draft.
  A specification begins as an Internet draft
  working document with no official status
  with a 6-month lifetime
RFC (Request for Comment)
  Upon recommendation from the Internet authorities, a draft may be published as a Request for Comment (RFC)
  Edited, assigned a number, and made available to all interested parties

## Slide 31: Internet Standards
Prior to approval, the proposed internet standard goes through a series of stages called a “standards track.” The standard first starts as a draft, which may evolve into an RFC (Request for Comments). If the IETF approves the RFC, then it becomes a standard.
RFCs and proposed internet standards cover a lot of ground. From standards for handling technical TCP/IP processes to standards for the display of various types of media, the IETF weighs in on a large number of these standards as they make their way toward adoption.
A list of proposed standards can be found at RFC-editor.org

## Slide 32: Home Works
Page 24
  Problems – 15, 16, 17, 19
Page 25
  Problems – 20, 22, 25, 26, 28, 29

## Slide 33: Reference
Data Communications and Networking
Behrouz A. Forouzan,
4th EditionMcGraw-Hill (Chap - 1)
A clear idea about Hub, Switches and Routers - https://www.youtube.com/watch?v=1z0ULvg_pW8